## Slide 1
DDCA GROUP PROJECT · TEAM 07
Digital Door Access
System Using
Combination Logic
A combinational-logic based electronic lock that verifies an access code and grants entry without any mechanical key.
TEAM MEMBERS
Manideep · Aarush · Hansika · Neelagreeva · Swarajith

## Slide 2
INTRODUCTION
What is a Digital Door Access System?
An electronic lock that replaces a conventional mechanical key with a secret access code entered on a keypad or switch bank.
The heart of the system is a combinational logic circuit — it has no memory of past inputs; the output depends only on the code present at that instant.
Each bit of the entered code is compared against a pre-set reference code using logic gates such NOT Gate & AND Gate, and the results are combined with an AND gate.
If — and only if — every bit matches, the circuit produces a single "Access Granted" signal that drives the door-unlocking mechanism.
Input → Logic → Action
Keypad code → gate-level comparison → relay-driven unlock
No microcontroller required for the core comparison — pure digital logic gates do the job.
DDCA · TEAM 7 · DIGITAL DOOR ACCESS SYSTEM
02

## Slide 3
PROBLEM STATEMENT
Why Move Away from Mechanical Locks?
Keys Get Lost or Copied
Physical keys can be misplaced, stolen, or duplicated without the owner's knowledge, creating a lasting security gap.
No Access Control
A mechanical lock cannot restrict entry to specific people or times — anyone holding the key can enter, anytime.
Slow to Reconfigure
Changing who can enter means changing the physical lock or re-cutting keys — costly and inconvenient.
Motivation:
Design a low-cost, reliable access-control circuit — built entirely from basic digital logic gates — that grants entry only when the correct code is presented.
DDCA · TEAM 7 · DIGITAL DOOR ACCESS SYSTEM
03

## Slide 4
OBJECTIVES
Project Objectives
01
Design the comparison logic
Build a combinational circuit that checks an entered code against a fixed reference code, bit by bit.
02
Use only basic logic gates
Implement the comparator using XNOR, AND, OR and NOT gates — no microcontroller in the core logic.
03
Drive a real unlocking action
Use the match output to energise a relay/solenoid that physically unlocks the door.
04
Verify with a truth table
Simulate and test every input combination to confirm the circuit only unlocks for the correct code.
DDCA · TEAM 7 · DIGITAL DOOR ACCESS SYSTEM
04

## Slide 5
SYSTEM DESIGN
System Block Diagram
Keypad /
Switch Input
Combinational
Comparator Logic
Code
Match?
Relay / Solenoid
→ Door Unlocks
Buzzer + Red LED
→ Access Denied
Green LED
Stays Lit
Yes
No
The comparator continuously checks the entered bits; a single AND-combined "match" signal decides which path the system takes.
DDCA · TEAM 7 · DIGITAL DOOR ACCESS SYSTEM
05

## Slide 6
LOGIC DESIGN
Combinational Logic & Truth Table
Bit-wise Comparison
Each entered bit (A, B, C) is compared to the corresponding reference bit using an XNOR gate — it outputs 1 only when the two bits are equal. The three XNOR outputs are combined with an AND gate so the final output Y is 1 only when all bits match.
Sample Truth Table (3-bit code, reference = 1 0 1)
A | B | C | Y (Unlock)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 1 | 0
Only the exact match 1-0-1 pulls the output high — every other combination keeps the door locked.
Here now, we only use AND Gate and NOT Gate for simple construction.
DDCA · TEAM 7 · DIGITAL DOOR ACCESS SYSTEM
06

## Slide 7
OPERATION
Working Flowchart
Start
User enters code
on keypad
Gates compare
each bit to reference
AND output
= 1 ?
Relay energised —
door unlocks + green LED
YES
Buzzer sounds +
red LED — access denied
NO
End
Purely Combinational
There is no clock or memory element — the decision is made instantly and continuously from the present input state alone. As soon as the correct code is removed, the output returns low.
DDCA · TEAM 7 · DIGITAL DOOR ACCESS SYSTEM
08

## Slide 8
IMPLEMENTATION
Components Used
Component | IC / Part | Function
Switches / Keypad | SPDT toggles or 4×3 matrix | Enter the access code as logic 0/1 inputs
AND Gate | 74LS08 | Combines all bit-comparisons into one match signal
Relay / Solenoid | 5V/12V relay module | Physically unlocks the door mechanism
Indicator LEDs | Green / Red LED | Shows access granted or denied
Power Supply | 5V regulated (7805) | Powers all logic ICs and the relay driver
DDCA · TEAM 7 · DIGITAL DOOR ACCESS SYSTEM
09

## Slide 9
APPLICATIONS
Where This System Can Be Used
Homes
Keyless entry for front doors and gates
Offices
Restricting entry to authorised staff only
Storerooms
Protecting inventory & equipment areas
Labs
Controlling access to sensitive lab equipment
Server Rooms
Guarding critical IT infrastructure
Lockers & Safes
Personal or shared secure storage
DDCA · TEAM 7 · DIGITAL DOOR ACCESS SYSTEM
10

## Slide 10
EVALUATION
Advantages & Limitations
Advantages
No physical key to lose, copy, or pick
Instant response — no processing delay
Simple, low-cost design using standard ICs
Access code changed easily by rewiring reference bits
Low power consumption, easy to maintain
Limitations
Fixed code — changing it needs rewiring, not reprogramming
No memory of failed attempts (purely combinational)
No built-in lockout after repeated wrong codes
Lower security than microcontroller / biometric systems
Wiring complexity grows with longer access codes
DDCA · TEAM 7 · DIGITAL DOOR ACCESS SYSTEM
11

## Slide 11
CONCLUSION
A Practical Case for
Combinational Logic
This project shows that a functional, real-world security device can be built from nothing more than AND, OR and NOT gates — no microcontroller needed for the core decision-making. The design was verified with a truth table covering every input combination, confirming the door unlocks only for the correct code, meeting the project's objectives of a low-cost, reliable, gate-level access-control system.
FUTURE SCOPE
Add sequential logic for lockout after failed attempts
Integrate a microcontroller + keypad matrix for reprogrammable codes
Extend with biometric or RFID / IoT-based access control
Team 07 · Manideep · Aarush · Hansika · Neelagreeva · Swarajith